## Slide 1: Cameras
Slide deck courtesy Svetlana Lazebnik

## Slide 2: Overview
The pinhole projection model
  Qualitative properties
  Perspective projection matrix
Cameras with lenses
  Depth of focus
  Field of view
  Lens aberrations
Digital cameras
  Sensors
  Color
  Artifacts

## Slide 3: Let’s design a camera
Idea 1: put a piece of film in front of an object
Do we get a reasonable image?
Slide by Steve Seitz

## Slide 4: Pinhole camera
Add a barrier to block off most of the rays
  This reduces blurring
  The opening is known as the aperture
Slide by Steve Seitz
Notes: It gets inverted

## Slide 5: Pinhole camera model
Pinhole model:
  Captures pencil of rays – all rays through a single point
  The point is called Center of Projection (focal point)
  The image is formed on the Image Plane
Slide by Steve Seitz

## Slide 6: Dimensionality reduction: from 3D to 2D
Figures © Stephen E. Palmer, 2002
3D world
2D image
What is preserved?
  Straight lines, incidence
What have we lost?
  Angles, lengths
Slide by A. Efros

## Slide 7: Projection properties
Many-to-one: any points along same visual ray map to same point in image
Points → points
  But projection of points on focal plane is undefined
Lines → lines (collinearity is preserved)
  But lines through focal point (visual rays) project to a point
Planes → planes (or half-planes)
  But planes through focal point project to lines

## Slide 8: Vanishing points
Each direction in space has its own vanishing point
  All lines going in that direction converge at that point
  Exception: directions parallel to the image plane

## Slide 9: Vanishing points
Each direction in space has its own vanishing point
  All lines going in that direction converge at that point
  Exception: directions parallel to the image plane
How do we construct the vanishing point of a line?
  What about the vanishing line of a plane?
image plane
camera
center
line on ground plane
vanishing point

## Slide 10: One-point perspective
Masaccio, Trinity, Santa Maria Novella, Florence, 1425-28
One of the first consistent uses of perspective in Western art

## Slide 11: Perspective distortion
Problem for architectural photography: converging verticals
Source: F. Durand

## Slide 12: Perspective distortion
Problem for architectural photography: converging verticals
Solution: view camera (lens shifted w.r.t. film)
Source: F. Durand
Tilting the camera upwards results in converging verticals
Keeping the camera level, with an ordinary lens, captures only the bottom portion of the building
Shifting the lens upwards results in a picture of the entire subject
http://en.wikipedia.org/wiki/Perspective_correction_lens

## Slide 13: Perspective distortion
Problem for architectural photography: converging verticals
Result:
Source: F. Durand

## Slide 14: Perspective distortion
What does a sphere project to?
Image source: F. Durand

## Slide 15: Perspective distortion
What does a sphere project to?

## Slide 16: Perspective distortion
The exterior columns appear bigger
The distortion is not due to lens flaws
Problem pointed out by Da Vinci
Slide by F. Durand

## Slide 17: Perspective distortion: People

## Slide 18: Modeling projection
The coordinate system
  The optical center (O) is at the origin
  The image plane is parallel to xy-plane (perpendicular to z axis)
Source: J. Ponce, S. Seitz
x
y
z
f
Notes: This way the image is right-side-up

## Slide 19: Modeling projection
Projection equations
  Compute intersection with image plane of ray from P = (x,y,z) to O
  Derived using similar triangles
Source: J. Ponce, S. Seitz
  We get the projection by throwing out the last coordinate:
x
y
z
f
Notes: The camera projection scales the apparent height of objects by the inverse of the depth. This results in the well-known effect that objects farther away from the camera look smaller.
We don’t care that the image is upside down: we can simply pretend that the image plane is in front of the camera center.

## Slide 20: Homogeneous coordinates
Is this a linear transformation?
Trick: add one more coordinate:
homogeneous image
coordinates
homogeneous scene
coordinates
Converting from homogeneous coordinates
  no—division by z is nonlinear
Slide by Steve Seitz

## Slide 21: Perspective Projection Matrix
Projection is a matrix multiplication using homogeneous coordinates

## Slide 22: Perspective Projection Matrix
divide by the third coordinate
Projection is a matrix multiplication using homogeneous coordinates

## Slide 23: Perspective Projection Matrix
divide by the third coordinate
Projection is a matrix multiplication using homogeneous coordinates
In practice: lots of coordinate transformations…
World to camera coord. trans. matrix (4x4)
Perspective projection matrix (3x4)
Camera to pixel coord. trans. matrix (3x3)
=
2D
point (3x1)
3D point (4x1)

## Slide 24: Orthographic Projection
Special case of perspective projection
  Distance from center of projection to image plane is infinite
  Also called “parallel projection”
  What’s the projection matrix?
Image
World
Slide by Steve Seitz
Notes: Is this a linear function?

## Slide 25: Building a real camera

## Slide 26: Camera Obscura
Basic principle known to Mozi (470-390 BCE), Aristotle (384-322 BCE)
Drawing aid for artists: described by Leonardo da Vinci (1452-1519)
Gemma Frisius, 1558
Source: A. Efros

## Slide 27: Abelardo Morell
Camera Obscura Image of Manhattan View Looking South in Large Room, 1996
http://www.abelardomorell.net/camera_obscura1.html
From Grand Images Through a Tiny Opening, Photo District News, February 2005

## Slide 28: Home-made pinhole camera
http://www.debevec.org/Pinhole/
Why so
blurry?
Slide by A. Efros

## Slide 29: Shrinking the aperture
Why not make the aperture as small as possible?
  Less light gets through
  Diffraction effects…
Slide by Steve Seitz

## Slide 30: Shrinking the aperture

## Slide 31: Adding a lens
A lens focuses light onto the film
  Thin lens model:
    Rays passing through the center are not deviated (pinhole projection model still holds)
Slide by Steve Seitz

## Slide 32: Adding a lens
A lens focuses light onto the film
  Thin lens model:
    Rays passing through the center are not deviated (pinhole projection model still holds)
    All parallel rays converge to one point on a plane located at the focal length f
Slide by Steve Seitz
focal point
f

## Slide 33: Adding a lens
A lens focuses light onto the film
  There is a specific distance at which objects are “in focus”
    other points project to a “circle of confusion” in the image
“circle of
confusion”
Slide by Steve Seitz

## Slide 34: Thin lens formula
What is the relation between the focal length (f), the distance of the object from the optical center (D), and the distance at which the object will be in focus (D’)?
f
D
D’
Slide by Frédo Durand
object
image plane
lens
Notes: This is the relation between the focal length (f), the distance of the object from the camera (D), and the distance at which the object will be in focus (D’)

## Slide 35: Thin lens formula
f
D
D’
Similar triangles everywhere!
Slide by Frédo Durand
object
image plane
lens

## Slide 36: Thin lens formula
f
D
D’
Similar triangles everywhere!
y’
y
y’/y = D’/D
Slide by Frédo Durand
object
image plane
lens

## Slide 37: Thin lens formula
f
D
D’
Similar triangles everywhere!
y’
y
y’/y = D’/D
y’/y = (D’-f)/f
Slide by Frédo Durand
object
image plane
lens

## Slide 38: Thin lens formula
f
D
D’
1
D’
D
1
1
f
+
=
Any point satisfying the thin lens equation is in focus.
Slide by Frédo Durand
object
image plane
lens
Notes: And the set of all such points forms a plane parallel to the image (plane of focus).

## Slide 39: Depth of Field
http://www.cambridgeincolour.com/tutorials/depth-of-field.htm
Slide by A. Efros
Notes: Depth of field is the range of distance within the subject that is acceptably sharp.

## Slide 40: How can we control the depth of field?
Changing the aperture size affects depth of field
  A smaller aperture increases the range in which the object is approximately in focus
  But small aperture reduces amount of light – need to increase exposure
Slide by A. Efros

## Slide 41: Varying the aperture
Large aperture = small DOF
Small aperture = large DOF
Slide by A. Efros

## Slide 42: Field of View
Slide by A. Efros
Notes: The field of view is the angular extent of the world that is observed by the camera.

## Slide 43: Field of View
Slide by A. Efros
What does FOV depend on?

## Slide 44: Field of View
f
Smaller FOV = larger Focal Length
Slide by A. Efros
f
FOV depends on focal length and size of the camera retina

## Slide 45: Field of View / Focal Length
Large FOV, small f
Camera close to car
Small FOV, large f
Camera far from the car
Sources: A. Efros, F. Durand

## Slide 46: Same effect for faces
standard
wide-angle
telephoto
Source: F. Durand

## Slide 47: Approximating an affine camera
Source: Hartley & Zisserman

## Slide 48: The dolly zoom
Continuously adjusting the focal length while the camera moves away from (or towards) the subject
http://en.wikipedia.org/wiki/Dolly_zoom

## Slide 49: The dolly zoom
Continuously adjusting the focal length while the camera moves away from (or towards) the subject
“The Vertigo shot”
Examples of dolly zoom from movies (YouTube)

## Slide 50: Real lenses

## Slide 51: Lens Flaws: Chromatic Aberration
Lens has different refractive indices for different wavelengths: causes color fringing
Near Lens Center
Near Lens Outer Edge

## Slide 52: Lens flaws: Spherical aberration
Spherical lenses don’t focus light perfectly
Rays farther from the optical axis focus closer

## Slide 53: Lens flaws: Vignetting

## Slide 54: Radial Distortion
No distortion
Pin cushion
Barrel
  Caused by imperfect lenses
  Deviations are most noticeable near the edge of the lens

## Slide 55: Digital camera
A digital camera replaces film with a sensor array
  Each cell in the array is light-sensitive diode that converts photons to electrons
  Two common types
    Charge Coupled Device (CCD)
    Complementary metal oxide semiconductor (CMOS)
  http://electronics.howstuffworks.com/digital-camera.htm
Slide by Steve Seitz

## Slide 56: Color sensing in camera: Color filter array
Source: Steve Seitz
Estimate missing components from neighboring values (demosaicing)
Why more green?
Bayer grid
Human Luminance Sensitivity Function

## Slide 57: Problem with demosaicing: color moire
Slide by F. Durand

## Slide 58: The cause of color moire
detector
Fine black and white detail in image
misinterpreted as color information
Slide by F. Durand

## Slide 59: Color sensing in camera: Prism
Requires three chips and precise alignment
More expensive
CCD(B)
CCD(G)
CCD(R)

## Slide 60: Color sensing in camera: Foveon X3
Source: M. Pollefeys
http://en.wikipedia.org/wiki/Foveon_X3_sensor
http://www.foveon.com/article.php?a=67
CMOS sensor
Takes advantage of the fact that red, blue and green light penetrate silicon to different depths
better image quality

## Slide 61: Digital camera artifacts
Noise
    low light is where you most notice noise
    light sensitivity (ISO) / noise tradeoff
    stuck pixels
In-camera processing
    oversharpening can produce halos
Compression
    JPEG artifacts, blocking
Blooming
    charge overflowing into neighboring pixels
Color artifacts
    purple fringing from microlenses,
    white balance
Slide by Steve Seitz

## Slide 62: Historic milestones
Pinhole model: Mozi (470-390 BCE), Aristotle (384-322 BCE)
Principles of optics (including lenses): Alhacen (965-1039 CE)
Camera obscura: Leonardo da Vinci (1452-1519), Johann Zahn (1631-1707)
First photo: Joseph Nicephore Niepce (1822)
Daguerréotypes (1839)
Photographic film (Eastman, 1889)
Cinema (Lumière Brothers, 1895)
Color Photography (Lumière Brothers, 1908)
Television (Baird, Farnsworth, Zworykin, 1920s)
First consumer camera with CCD Sony Mavica (1981)
First fully digital camera: Kodak DCS100 (1990)
Niepce, “La Table Servie,” 1822
CCD chip
Alhacen’s notes

## Slide 63: Early color photography
Sergey Prokudin-Gorskii (1863-1944)
Photographs of the Russian empire (1909-1916)
Assignment 1 (due February 1)!
http://www.loc.gov/exhibits/empire/
http://en.wikipedia.org/wiki/Sergei_Mikhailovich_Prokudin-Gorskii
Lantern
projector

## Slide 64: First digitally scanned photograph
1957, 176x176 pixels
http://listverse.com/history/top-10-incredible-early-firsts-in-photography/